## Slide 1
Is it timeout?
Subscribe to TRANSMISSION
start
Notification
Transmission ends as Failed.
Sleep for 0.001 sec.
Is the monitor field registered as Success?
Trigger the RF front-end to transmit the packet.
Create a monitor field for recording the result of the packet.
(Waiting/Failed/Success)
Is the RF front-end idle?
The transmission ends as Success
Remove the oldest member from the message queue and trigger the Queue Agent to issue another transmission.
Has it exceeded the max retry?
Yes
Yes
Yes
Yes
No
No
No

## Slide 2
Subscribe to QUEUE:LIST:TRANS
start
Does the information have the correct format?
Notification
Sleep for 0.001s
Discard
Is the RF front-end idle?
Wait for the subscribed key to be triggered.
Issue a transmission request to Transmission Agent. Then, set the RF front-end to be busy.
Yes
Yes
Yes
No
No

## Slide 3
text
elif header is DATA_FRAME:
reply_with_ack()
set_to_db()
ack_frame = scapy.Dot11FCS(addr1=addr, type=1, subtype=13, FCfield=0)
sock.sendto(bytes(ack_frame), (localhost, 52001))
timestamp = time.time()
db.hmset(“Recv:seq:timestamp”, {“payload”: payload, “info”:info})
db.set(“CSI:timestamp”, csi_json)
db.set(“CSI:ACTION:CSI”, “CSI:timestamp”)
if payload has ControlType:
if payload[“ControlType”] == “HOP”:
if payload[“ControlAction”].isdigit():
db.set(“RFSYSTEM:STATE”, “Hold”)
db.hset(“SYSTEM:HOPPING”, “Stage”, 4)
action_to_hop(payload)
elif header is CTRL_FRAME:
action_to_ack()
ACK_STATE = db.get(“TRANS:ACK”)
if ACK_STATE == “Waiting”:
db.set(“TRANS:ACK”, “Success”)
db.set(“RFDEVICE:STATE”, “Idle”)
db.rpop(“QUEUE:LIST:TRANS”)
db.set(“SYSTEM:ACTION:HOP”, payload)
while db.exists(“QUEUE:LIST:TRANS”):
rf_state = db.get(“RFDEVICE:STATE”)
sys_state = db.get(“RFSYSTEM:STATE”)
oldest_key = db.lrange(“QUEUE:LIST:TRANS”, -1, -1)
ack_for_key = db.get(“oldest_key:ACK”)
if ack_for_key is not None:
if db.get(ack_for_key) == “Failed”:
db.rpop(“QUEUE:LIST:TRANS”)
elif rf_state == “Idle”:
oldest_key = db.lrange(“QUEUE:LIST:TRANS”, -1, -1)
db.set(“Transmission”, oldest_key)
db.set(“RFDEVICE:STATE”, “Busy”)
elif sys_state == “Hold”:
time.sleep(0.01)
else:
time.sleep(0.001)
db_key = self.get(“Transmission”)
if db.get(“RFDEVICE:STATE”) != “Busy”:
db.set(“RFDEVICE:STATE”, “Busy”)
db.set(“Trans:db_key”, trans_msg)
db.set(“TRANS:ACK”, “Waiting”)
monitor_key()
while retry < RETRY_MAX:
if db.get(“RFSYSTEM:STATE”) == “Hold”:
return
elif db.get(“TRANS:ACK”) != “Waiting”
return
elif wait_time < MAX_TIME:
time.sleep(wait_ interval)
wait_time += wait_interval
else:
retry += 1
wait_time = 0
db.delete(“Trans:db_key”)
db.set(“Trans:db_key”, trans_msg)
abort_monitor()
db.set(“RECEPTION”, db_key)
db.set(“db_key:ACK”, “Fail”)
db.set(“RFDEVICE:STATE”, “Idle”)
db.set(“TRANS:ACK”, “Failed”)
db.rpop(“QUEUE:LIST:TRANS”)
if action == “CSI”:
csi_key = db.get(“SYSTEM:ACTION:CSI”)
db.lpush(“SYSTEM:CSI:QUEUE”, csi_key)
if len(db.lrange(“SYSTEM:CSI:QUEUE”, 0, -1)) > CSI_Q_MAX:
oldest_csi_key = db.rpop(“SYSTEM:CSI:QUEUE”)
db.delete(oldest_csi_key)
detect_interference()
elif action == “HOP”:
action_to_hop()
elif action == “CEHCK”:
if msg[“data”] != “expired”:
return
if db.get(“SYSTEM:ACTION:CHECK”) is not None:
return
if db.get(“HOPPING_CTRL_ACT_NEW_FREQ_ACK”) is not None:
return
else:
old_freq = db.get(“SYSTEM:FREQ”)
db.hset(“TuneRF:11”, “Freq”, old_freq)
db.set(“RFSYSTEM:STATE”, “Free”)
db.set(“RFDEVICE:STATE”, “Idle”)
elif action == “DEBUG”:
detect_interference()
if detected:
db.hset(“SYSTEM:HOPPING”, “Stage”, 2)
db.set(“SYSTEM:STATE”, “Hold”)
hop_to = 2442000000
pre_freq = db.get(“SYSTEM:FREQ”)
for i in range(5):
db.hmset(“SYSTEM:HOPPING”, {“Role”: “Initiator”, “Stage”: 3, “Freq”: hop_to, “PreFreq”: pre_freq})
db.set(“Trans:FREQ:HOP”, {“ControlType”: “HOP”, “ControlAction”: hop_to}, “Role”: “Follower”)
time.sleep(0.01)
db.hmset(“TuneRF:11”, {“Freq”: hop_to, “Gain”: 0.4})
db.set(“SYSTEM:ACTION:CHECK”, “True”, ex=10)
role = db.hget(“SYSTEM:HOPPING”, “Role”)
if role == “Initiator”:
if payload[“ControlAction”] == “HOLD:ACK”:
hop_to = db.hget(“SYSTEM:HOPPING”, “Freq”)
db.hset(“TuneRF:11”, Freq, hop_to)
for i in range(5):
db.set(“Trans:FREQ:HOP”, json)
hset(“SYSTEM:HOPPING”, Stage, 8)
time.sleep(0.01)
elif payload[“ControlAction”] == “NEW:FREQ:ACK”:
db.delete(“SYSTEM:ACTION:CHECK”)
db.set(“RFSYSTEM:STATE”, “Free”)
else:
if stage == 4:
pre_fre = db.get(“SYSTEM:FREQ”)
db.set(“Trans:FREQ:HOP”, json)
db.hset(“SYSTEM:HOPPING”, Stage, 5)
time.sleep(wait_time)
db.hset(“TuneRF:11”, Freq, hop_to)
db.hmset(“SYSTEM:HOPPING”, {Stage: 6, PreFreq: pre_freq, Freq: payload[“ControlAction”]})
elif stage == 6:
for i in range(5):
db.set(“Trans:FREQ:HOP”, json)
db.hset(“SYSTEM:HOPPING”, Stage, 9)
time.sleep(0.01)
time.sleep(0.5)
db.set(“RFSYSTEM:STATE”, Free)
Queue
Trans
Action
Sink

## Slide 4
elif header is DATA_FRAME:
reply_with_ack()
set_to_db()
ack_frame = scapy.Dot11FCS(addr1=addr, type=1, subtype=13, FCfield=0)
sock.sendto(bytes(ack_frame), (localhost, 52001))
timestamp = time.time()
db.hmset(“Recv:seq:timestamp”, {“payload”: payload, “info”:info})
db.set(“CSI:timestamp”, csi_json)
db.set(“CSI:ACTION:CSI”, “CSI:timestamp”)
if payload has ControlType:
if payload[“ControlType”] == “HOP”:
if payload[“ControlAction”].isdigit():
db.set(“RFSYSTEM:STATE”, “Hold”)
db.hset(“SYSTEM:HOPPING”, “Stage”, 4)
action_to_hop(payload)
elif header is CTRL_FRAME:
action_to_ack()
ACK_STATE = db.get(“TRANS:ACK”)
if ACK_STATE == “Waiting”:
db.set(“TRANS:ACK”, “Success”)
db.set(“RFDEVICE:STATE”, “Idle”)
db.rpop(“QUEUE:LIST:TRANS”)
db.set(“SYSTEM:ACTION:HOP”, payload)
while db.exists(“QUEUE:LIST:TRANS”):
rf_state = db.get(“RFDEVICE:STATE”)
sys_state = db.get(“RFSYSTEM:STATE”)
oldest_key = db.lrange(“QUEUE:LIST:TRANS”, -1, -1)
ack_for_key = db.get(“oldest_key:ACK”)
if ack_for_key is not None:
if db.get(ack_for_key) == “Failed”:
db.rpop(“QUEUE:LIST:TRANS”)
elif rf_state == “Idle”:
oldest_key = db.lrange(“QUEUE:LIST:TRANS”, -1, -1)
db.set(“Transmission”, oldest_key)
db.set(“RFDEVICE:STATE”, “Busy”)
elif sys_state == “Hold”:
time.sleep(0.01)
else:
time.sleep(0.001)
db_key = self.get(“Transmission”)
if db.get(“RFDEVICE:STATE”) != “Busy”:
db.set(“RFDEVICE:STATE”, “Busy”)
db.set(“Trans:db_key”, trans_msg)
db.set(“TRANS:ACK”, “Waiting”)
monitor_key()
while retry < RETRY_MAX:
if db.get(“RFSYSTEM:STATE”) == “Hold”:
return
elif db.get(“TRANS:ACK”) != “Waiting”
return
elif wait_time < MAX_TIME:
time.sleep(wait_ interval)
wait_time += wait_interval
else:
retry += 1
wait_time = 0
db.delete(“Trans:db_key”)
db.set(“Trans:db_key”, trans_msg)
abort_monitor()
db.set(“RECEPTION”, db_key)
db.set(“db_key:ACK”, “Fail”)
db.set(“RFDEVICE:STATE”, “Idle”)
db.set(“TRANS:ACK”, “Failed”)
db.rpop(“QUEUE:LIST:TRANS”)
if action == “CSI”:
csi_key = db.get(“SYSTEM:ACTION:CSI”)
db.lpush(“SYSTEM:CSI:QUEUE”, csi_key)
if len(db.lrange(“SYSTEM:CSI:QUEUE”, 0, -1)) > CSI_Q_MAX:
oldest_csi_key = db.rpop(“SYSTEM:CSI:QUEUE”)
db.delete(oldest_csi_key)
detect_interference()
elif action == “HOP”:
action_to_hop()
elif action == “CEHCK”:
if msg[“data”] != “expired”:
return
if db.get(“SYSTEM:ACTION:CHECK”) is not None:
return
if db.get(“HOPPING_CTRL_ACT_NEW_FREQ_ACK”) is not None:
return
else:
old_freq = db.get(“SYSTEM:FREQ”)
db.hset(“TuneRF:11”, “Freq”, old_freq)
db.set(“RFSYSTEM:STATE”, “Free”)
db.set(“RFDEVICE:STATE”, “Idle”)
elif action == “DEBUG”:
detect_interference()
if detected:
db.hset(“SYSTEM:HOPPING”, “Stage”, 2)
db.set(“SYSTEM:STATE”, “Hold”)
hop_to = 2442000000
pre_freq = db.get(“SYSTEM:FREQ”)
for i in range(5):
db.hmset(“SYSTEM:HOPPING”, {“Role”: “Initiator”, “Stage”: 3, “Freq”: hop_to, “PreFreq”: pre_freq})
db.set(“Trans:FREQ:HOP”, {“ControlType”: “HOP”, “ControlAction”: hop_to}, “Role”: “Follower”)
time.sleep(0.01)
db.hmset(“TuneRF:11”, {“Freq”: hop_to, “Gain”: 0.4})
db.set(“SYSTEM:ACTION:CHECK”, “True”, ex=10)
role = db.hget(“SYSTEM:HOPPING”, “Role”)
if role == “Initiator”:
if payload[“ControlAction”] == “HOLD:ACK”:
hop_to = db.hget(“SYSTEM:HOPPING”, “Freq”)
db.hset(“TuneRF:11”, Freq, hop_to)
for i in range(5):
db.set(“Trans:FREQ:HOP”, json)
hset(“SYSTEM:HOPPING”, Stage, 8)
time.sleep(0.01)
elif payload[“ControlAction”] == “NEW:FREQ:ACK”:
db.delete(“SYSTEM:ACTION:CHECK”)
db.set(“RFSYSTEM:STATE”, Free)
else:
if stage == 4:
pre_fre = db.get(“SYSTEM:FREQ”)
db.set(“Trans:FREQ:HOP”, json)
db.hset(“SYSTEM:HOPPING”, Stage, 5)
time.sleep(wait_time)
db.hset(“TuneRF:11”, Freq, hop_to)
db.hmset(“SYSTEM:HOPPING”, {Stage: 6, PreFreq: pre_freq, Freq: payload[“ControlAction”]})
elif stage == 6:
for i in range(5):
db.set(“Trans:FREQ:HOP”, json)
db.hset(“SYSTEM:HOPPING”, Stage, 9)
time.sleep(0.01)
time.sleep(0.5)
db.set(“RFSYSTEM:STATE”, Free)
Queue
Trans
Action
Sink
text
1
3
8
4
6
5

## Slide 5
Hop to new frequency.
Trying a predefined packet.
Wait for ACK
Sending Packets
Rx
Tx
Sending Packets
Timeout receiving ACK
Detect Interference
Jump to the new frequency and wait.
Receive on new channel.
Must be successful.
Receive ACK on new channel.
Must be successful.
Hop to new frequency.
Trying a predefined packet.
Wait for ACK
Sending Packets
Sending Packets
Timeout receiving ACK
Detect Interference
Jump to the new frequency and wait.
Don’t receive on new channel.
Might be failed.
Return to last channel
Not receiving ACK on new channel.
Might be failed.

## Slide 6
text
elif header is DATA_FRAME:
reply_with_ack()
set_to_db()
ack_frame = scapy.Dot11FCS(addr1=addr, type=1, subtype=13, FCfield=0)
sock.sendto(bytes(ack_frame), (localhost, 52001))
timestamp = time.time()
db.hmset(“Recv:seq:timestamp”, {“payload”: payload, “info”:info})
db.set(“CSI:timestamp”, csi_json)
db.set(“CSI:ACTION:CSI”, “CSI:timestamp”)
if payload has ControlType:
if payload[“ControlType”] == “HOP”:
if payload[“ControlAction”].isdigit():
db.set(“RFSYSTEM:STATE”, “Hold”)
db.hset(“SYSTEM:HOPPING”, “Stage”, 4)
action_to_hop(payload)
elif header is CTRL_FRAME:
action_to_ack()
ACK_STATE = db.get(“TRANS:ACK”)
if ACK_STATE == “Waiting”:
db.set(“TRANS:ACK”, “Success”)
db.set(“RFDEVICE:STATE”, “Idle”)
db.rpop(“QUEUE:LIST:TRANS”)
db.set(“SYSTEM:ACTION:HOP”, payload)
while db.exists(“QUEUE:LIST:TRANS”):
rf_state = db.get(“RFDEVICE:STATE”)
sys_state = db.get(“RFSYSTEM:STATE”)
oldest_key = db.lrange(“QUEUE:LIST:TRANS”, -1, -1)
ack_for_key = db.get(“oldest_key:ACK”)
if ack_for_key is not None:
if db.get(ack_for_key) == “Failed”:
db.rpop(“QUEUE:LIST:TRANS”)
elif rf_state == “Idle”:
oldest_key = db.lrange(“QUEUE:LIST:TRANS”, -1, -1)
db.set(“Transmission”, oldest_key)
db.set(“RFDEVICE:STATE”, “Busy”)
elif sys_state == “Hold”:
time.sleep(0.01)
else:
time.sleep(0.001)
db_key = self.get(“Transmission”)
if db.get(“RFDEVICE:STATE”) != “Busy”:
db.set(“RFDEVICE:STATE”, “Busy”)
db.set(“Trans:db_key”, trans_msg)
db.set(“TRANS:ACK”, “Waiting”)
monitor_key()
while retry < RETRY_MAX:
if db.get(“RFSYSTEM:STATE”) == “Hold”:
return
elif db.get(“TRANS:ACK”) != “Waiting”
return
elif wait_time < MAX_TIME:
time.sleep(wait_ interval)
wait_time += wait_interval
else:
retry += 1
wait_time = 0
db.delete(“Trans:db_key”)
db.set(“Trans:db_key”, trans_msg)
abort_monitor()
db.set(“RECEPTION”, db_key)
db.set(“db_key:ACK”, “Fail”)
db.set(“RFDEVICE:STATE”, “Idle”)
db.set(“TRANS:ACK”, “Failed”)
db.rpop(“QUEUE:LIST:TRANS”)
if action == “CSI”:
csi_key = db.get(“SYSTEM:ACTION:CSI”)
db.lpush(“SYSTEM:CSI:QUEUE”, csi_key)
if len(db.lrange(“SYSTEM:CSI:QUEUE”, 0, -1)) > CSI_Q_MAX:
oldest_csi_key = db.rpop(“SYSTEM:CSI:QUEUE”)
db.delete(oldest_csi_key)
detect_interference()
elif action == “HOP”:
action_to_hop()
elif action == “CEHCK”:
if msg[“data”] != “expired”:
return
if db.get(“SYSTEM:ACTION:CHECK”) is not None:
return
if db.get(“HOPPING_CTRL_ACT_NEW_FREQ_ACK”) is not None:
return
else:
old_freq = db.get(“SYSTEM:FREQ”)
db.hset(“TuneRF:11”, “Freq”, old_freq)
db.set(“RFSYSTEM:STATE”, “Free”)
db.set(“RFDEVICE:STATE”, “Idle”)
elif action == “DEBUG”:
detect_interference()
if detected:
db.hset(“SYSTEM:HOPPING”, “Stage”, 2)
db.set(“SYSTEM:STATE”, “Hold”)
hop_to = 2442000000
pre_freq = db.get(“SYSTEM:FREQ”)
for i in range(5):
db.hmset(“SYSTEM:HOPPING”, {“Role”: “Initiator”, “Stage”: 3, “Freq”: hop_to, “PreFreq”: pre_freq})
db.set(“Trans:FREQ:HOP”, {“ControlType”: “HOP”, “ControlAction”: hop_to}, “Role”: “Follower”)
time.sleep(0.01)
db.hmset(“TuneRF:11”, {“Freq”: hop_to, “Gain”: 0.4})
db.set(“SYSTEM:ACTION:CHECK”, “True”, ex=10)
role = db.hget(“SYSTEM:HOPPING”, “Role”)
if role == “Initiator”:
if payload[“ControlAction”] == “HOLD:ACK”:
hop_to = db.hget(“SYSTEM:HOPPING”, “Freq”)
db.hset(“TuneRF:11”, Freq, hop_to)
for i in range(5):
db.set(“Trans:FREQ:HOP”, json)
hset(“SYSTEM:HOPPING”, Stage, 8)
time.sleep(0.01)
elif payload[“ControlAction”] == “NEW:FREQ:ACK”:
db.delete(“SYSTEM:ACTION:CHECK”)
db.set(“RFSYSTEM:STATE”, “Free”)
else:
if stage == 4:
pre_fre = db.get(“SYSTEM:FREQ”)
db.set(“Trans:FREQ:HOP”, json)
db.hset(“SYSTEM:HOPPING”, Stage, 5)
time.sleep(wait_time)
db.hset(“TuneRF:11”, Freq, hop_to)
db.hmset(“SYSTEM:HOPPING”, {Stage: 6, PreFreq: pre_freq, Freq: payload[“ControlAction”]})
elif stage == 6:
for i in range(5):
db.set(“Trans:FREQ:HOP”, json)
db.hset(“SYSTEM:HOPPING”, Stage, 9)
time.sleep(0.01)
time.sleep(0.5)
db.set(“RFSYSTEM:STATE”, Free)
Queue
Trans
Action
Sink

## Slide 7
text
elif header is DATA_FRAME:
reply_with_ack()
set_to_db()
ack_frame = scapy.Dot11FCS(addr1=addr, type=1, subtype=13, FCfield=0)
sock.sendto(bytes(ack_frame), (localhost, 52001))
timestamp = time.time()
db.hmset(“Recv:seq:timestamp”, {“payload”: payload, “info”:info})
db.set(“CSI:timestamp”, csi_json)
db.set(“CSI:ACTION:CSI”, “CSI:timestamp”)
if payload has ControlType:
if payload[“ControlType”] == “HOP”:
if payload[“ControlAction”].isdigit():
db.set(“RFSYSTEM:STATE”, “Hold”)
db.hset(“SYSTEM:HOPPING”, “Stage”, 4)
action_to_hop(payload)
elif header is CTRL_FRAME:
action_to_ack()
ACK_STATE = db.get(“TRANS:ACK”)
if ACK_STATE == “Waiting”:
db.set(“TRANS:ACK”, “Success”)
db.set(“RFDEVICE:STATE”, “Idle”)
db.rpop(“QUEUE:LIST:TRANS”)
db.set(“SYSTEM:ACTION:HOP”, payload)
while db.exists(“QUEUE:LIST:TRANS”):
rf_state = db.get(“RFDEVICE:STATE”)
sys_state = db.get(“RFSYSTEM:STATE”)
oldest_key = db.lrange(“QUEUE:LIST:TRANS”, -1, -1)
ack_for_key = db.get(“oldest_key:ACK”)
if ack_for_key is not None:
if db.get(ack_for_key) == “Failed”:
db.rpop(“QUEUE:LIST:TRANS”)
elif rf_state == “Idle”:
oldest_key = db.lrange(“QUEUE:LIST:TRANS”, -1, -1)
db.set(“Transmission”, oldest_key)
db.set(“RFDEVICE:STATE”, “Busy”)
elif sys_state == “Hold”:
time.sleep(0.01)
else:
time.sleep(0.001)
db_key = self.get(“Transmission”)
if db.get(“RFDEVICE:STATE”) != “Busy”:
db.set(“RFDEVICE:STATE”, “Busy”)
db.set(“Trans:db_key”, trans_msg)
db.set(“TRANS:ACK”, “Waiting”)
monitor_key()
while retry < RETRY_MAX:
if db.get(“RFSYSTEM:STATE”) == “Hold”:
return
elif db.get(“TRANS:ACK”) != “Waiting”
return
elif wait_time < MAX_TIME:
time.sleep(wait_ interval)
wait_time += wait_interval
else:
retry += 1
wait_time = 0
db.delete(“Trans:db_key”)
db.set(“Trans:db_key”, trans_msg)
abort_monitor()
db.set(“RECEPTION”, db_key)
db.set(“db_key:ACK”, “Fail”)
db.set(“RFDEVICE:STATE”, “Idle”)
db.set(“TRANS:ACK”, “Failed”)
db.rpop(“QUEUE:LIST:TRANS”)
if action == “CSI”:
csi_key = db.get(“SYSTEM:ACTION:CSI”)
db.lpush(“SYSTEM:CSI:QUEUE”, csi_key)
if len(db.lrange(“SYSTEM:CSI:QUEUE”, 0, -1)) > CSI_Q_MAX:
oldest_csi_key = db.rpop(“SYSTEM:CSI:QUEUE”)
db.delete(oldest_csi_key)
detect_interference()
elif action == “HOP”:
action_to_hop()
elif action == “CEHCK”:
if msg[“data”] != “expired”:
return
if db.get(“SYSTEM:ACTION:CHECK”) is not None:
return
if db.get(“HOPPING_CTRL_ACT_NEW_FREQ_ACK”) is not None:
return
else:
old_freq = db.get(“SYSTEM:FREQ”)
db.hset(“TuneRF:11”, “Freq”, old_freq)
db.set(“RFSYSTEM:STATE”, “Free”)
db.set(“RFDEVICE:STATE”, “Idle”)
elif action == “DEBUG”:
detect_interference()
if detected:
db.hset(“SYSTEM:HOPPING”, “Stage”, 2)
db.set(“SYSTEM:STATE”, “Hold”)
hop_to = 2442000000
pre_freq = db.get(“SYSTEM:FREQ”)
for i in range(5):
db.hmset(“SYSTEM:HOPPING”, {“Role”: “Initiator”, “Stage”: 3, “Freq”: hop_to, “PreFreq”: pre_freq})
db.set(“Trans:FREQ:HOP”, {“ControlType”: “HOP”, “ControlAction”: hop_to}, “Role”: “Follower”)
time.sleep(0.01)
db.hmset(“TuneRF:11”, {“Freq”: hop_to, “Gain”: 0.4})
db.set(“SYSTEM:ACTION:CHECK”, “True”, ex=10)
role = db.hget(“SYSTEM:HOPPING”, “Role”)
if role == “Initiator”:
if payload[“ControlAction”] == “HOLD:ACK”:
hop_to = db.hget(“SYSTEM:HOPPING”, “Freq”)
db.hset(“TuneRF:11”, Freq, hop_to)
for i in range(5):
db.set(“Trans:FREQ:HOP”, json)
hset(“SYSTEM:HOPPING”, Stage, 8)
time.sleep(0.01)
elif payload[“ControlAction”] == “NEW:FREQ:ACK”:
db.delete(“SYSTEM:ACTION:CHECK”)
db.set(“RFSYSTEM:STATE”, “Free”)
else:
if stage == 4:
pre_fre = db.get(“SYSTEM:FREQ”)
db.set(“Trans:FREQ:HOP”, json)
db.hset(“SYSTEM:HOPPING”, Stage, 5)
time.sleep(wait_time)
db.hset(“TuneRF:11”, Freq, hop_to)
db.hmset(“SYSTEM:HOPPING”, {Stage: 6, PreFreq: pre_freq, Freq: payload[“ControlAction”]})
elif stage == 6:
for i in range(5):
db.set(“Trans:FREQ:HOP”, json)
db.hset(“SYSTEM:HOPPING”, Stage, 9)
time.sleep(0.01)
time.sleep(0.5)
db.set(“RFSYSTEM:STATE”, Free)
Queue
Trans
Action
Sink